## Slide 1: Evolvement of Fecal Sludge Management (FSM) at Rohingya Response, Cox’s Bazar
29th November, 2023

## Slide 2
Presentation Outline
Overview of Cox’s Bazar Rohingya Response – Jafar, WASH Sector
Containment – Jafar, WASH Sector
Collection and Transportation – Mejbah, IFRC
Treatment and Reuse/Disposal – Niloy, Oxfam
Effluent Quality Monitoring – Jafar, WASH Sector
Innovation and Learning – Niloy, Oxfam
WASH Sector Resources Doc’s on FSM – Niloy, Oxfam

## Slide 3
Overview of Cox’s Bazar Rohingya Response
Containment
Jafar Ikbal
WASH Engineer
WASH Sector, Bangladesh
jafar.ikbal@brac.net

## Slide 4
Coordination
Sanitation TWiG Formation (2017 to 2019)
Ad Hoc Group on Sanitation (2020 to 2022)
Technical Consultation Group Formation
(2023)
August, 2017 – 0.76 M Rohingya community have arrived at Cox’s Bazar
Currently 0.97M population within 33 Camps
3 UN, 20 INGO and NGO are working
Tropical climate (monsoon season – May to September)
Hilly terrain
Overview of Cox’s Bazar Rohingya Response

## Slide 5
Containment
Emergency
In 2017 , the first priority:
  Emergency Latrines Construction – dia 0.75m to 0.9m and depth 1m to 1.5m
  Super Structure – bamboo and tarpaulin
  Ensure Initial access to latrine
  Reduce Open Deification
Post Emergency:
In 2018, unified latrine design have been developed & considered:
  Community Needs and Desing Harmonization
  Containment type - Single Pit, Twin Pit, Septic Tank, Bio Fill & Bio Gas
  Super structure – wooden frame
  Generation Rate
  Gender and Person with Disability inclusion
Single Pit Latrine
Septic Tank Latrine
Twin Pit Latrine
Emergency
Phase
Gradual
upgradation
Shallow Tubewell
Tap Stand
Deep Tube
Well

## Slide 6
Containment
In 2023, unified latrine design have been updated with a comprehensive guideline & considered :
  Community needs
  Containment type - Single Pit, Twin Pit, Septic Tank
  Super structure – wooden and steel frame
  Generation Rate, Soil condition
  Low O & M costs
  Space Limitation
  Disaster resistance (like fire, cyclone)
Community engagement for O & M and ownership
Gender and Person with Disability inclusion
User Committee Member List
Steel Framed Single Pit Larine

## Slide 7
Collection and Transportation
Mejbah Uddin Chowdhury
Manager, Water, Sanitation & Hygiene
IFRC, Bangladesh
Mejbah.CHOWDHURY@ifrc.org

## Slide 8
Collection and Transportation
Mode of Collection & Transportation
Manual
Mechanical
Diaphragm Pump
Bucket
Vacutug
Drainage
Pump
Human + Drum
Pull/Push – Cart
Intermediate Faecal Sludge Transfer Network
Vacutug/Truck Load with Tank
Drum/Small Tank + Pickup
Collection
Transportation
Robin
Pump

## Slide 9
Emptying/Collection/Desludging

## Slide 10
Transportation

## Slide 11
Intermediate Faecal Sludge Transfer Network (IFSTN)
Transportation

## Slide 12
29,718 m3 of FS is transferred per month (26% average increase in wet season)
The most used transportation mode is Pit transfer/temporary pipe and pump
Intermediate Faecal Sludge Transfer Network (IFSTN) as the most cost-effective (ARUP, 2022)
Recommendations, Challenges and Others:
Avoid Manual desludging (bucket)
Use desludging pump
Safety/health rules/Ensure PPE
Challenge: accumulative solid sludge in pits + solid waste creating blockage
Desludging rate every 2 months on average (based on volume/population/type of latrine)
Collection and Transportation

## Slide 13
Treatment and Reuse/Disposal
Safwatul Haque Niloy
Sanitation Coordinator
OXFAM, Bangladesh
SNiloy@oxfam.org.uk

## Slide 14
Treatment
First phase emergency, How FS was managed ! 1. Excavate another pit ,transfer & backfill. 2. Open Desludging ponds. 3. Geo bags , mobile lime stabilization.
ODP
Geo Tube

## Slide 15
Treatment
FSTP -1
FSTP -2
FSTP -3
UKHIYA – Camps
Teknaf – Camps
IFSTN -1
120,000 Population
IFSTN -2
150,000 population
IFSTN -3
80,000 Population
Decentralized FSTP’s
Capacity 5 to 10 m3 ,
Each camp is served by avg. 8 to 12 unit
Centralized vs Decentralized FSM approach

## Slide 16
Treatment
Technologies
Biological
Anaerobic Baffled Reactor
Planted Drying Bed
Constructed Wetland
Up Flow Filter
DEWATS
Waste Stabilization Pond
Aerobic Treatment
Anaerobic Lagoon
Others
Chemical Treatment :
Lime Stabilization
High Tech : Omni Processor
Aeration
Lime Stabilization
DEWATS
WSP
ABR
Up Flow Filter
Mega FSTP 1
Mega FSTP 2
Omni Processor

## Slide 17
Treatment
Source : FSM technical assessment report ,2022 - ARUP , OXFAM , WASH Sector
Comparison of different systems

## Slide 18
Reuse/Disposal
Less progress compared to other stages of value chain.
Current practice limited to landfilling, incineration & pilot scale co composting , biogas to electricity , cooking projects
Challenges -
Space limitation was noted as a constraint for safely disposed or reuse the final solids.
Need to understand market, country policies and acceptability for sludge products (compost, gas etc)
Co Composting
Incineration

## Slide 19
Effluent Quality Monitoring
Jafar Ikbal
WASH Engineer
WASH Sector, Bangladesh
jafar.ikbal@brac.net

## Slide 20
Effluent Monitoring
In 2019 Waste Water monitoring framework have developed to monitor the effluent quality
In 2022 a central fecal sludge lab (FS lab) have developed (under Department of Public Health Engineering, Cox’s Bazar, Bangladesh) to monitor the effluent quality.
Following parameter have been tested thrice in a year through FS lab
Parameter | Range
pH | 6 to 9
BOD (mg/L) | 30
COD (mg/L) | 125
Nitrate (mg/L) | 50
Phosphate (mg/L) | 15
Suspended Solid (mg/L) | 100
Temperature ( ̊C) | 30
Total Coliform (cfu/100 mL) | 1000

## Slide 21
Effluent Monitoring
Mid of 2022 - Online FSTP Effluent Quality Monitoring Dashboard have developed
FSTP Effluent Sample Collection
Fecal Sludge Laboratory

## Slide 22
Innovation and Learning
WASH Sector Resources Doc’s on FSM
Safwatul Haque Niloy
Sanitation Coordinator
OXFAM, Bangladesh
SNiloy@oxfam.org.uk

## Slide 23
Innovation
PIT INTELLIGENT TRACKET ( PIT APP)

## Slide 24
Learning
Copying FSTP design and BoQ from other context without analysis can significantly affect performance & eventually fail ( faecal sludge ≠ waste water , FS from urban context ≠ Emergency) )
Poor N and P removal of current FSTP’s , do they even designed to meet standards !
Future FS projection is important to design the capacity of treatment plant, factors- containment type, soil characteristics, user behavior , water usage etc.
Plan for solid storage , treatment and final disposal from FSTP .
Maintaining operational parameters . Example : Up flow velocity of an ABR
Capacity building trainings for FSTP operators

## Slide 25
WASH Sector Resources Doc’s on FSM
WASH Sector Website – Link
Fecal Sludge Management (FSM) Strategy for Rohingya Response 2023 – Link
Phase 1 Technical Assessment of FSM in the Rohingya Response 2020 by ARUP – Link
Phase 2 Technical Assessment of FSM in the Rohingya Response 2022 by ARUP – Link
Approved Unified Latrine and Handwashing Stations Design 2023 – Link
Waste Water Monitoring Framework 2019 – Link
Mode of Operation of Fecal Sludge Laboratory Cox's Bazar 2023 – Link
FSTP Effluent Quality Monitoring Dashboard – Link
FSTP Location Map – Link
Latrine Location Map – Link

## Slide 26
THANK YOU
Jafar Ikbal
WASH Engineer
WASH Sector, Bangladesh
jafar.ikbal@brac.net
Safwatul Haque Niloy
Sanitation Coordinator
OXFAM, Bangladesh
SNiloy@oxfam.org.uk
Mejbah Uddin Chowdhury
Manager, Water, Sanitation & Hygiene
IFRC, Bangladesh
Mejbah.CHOWDHURY@ifrc.org